SECTION 116843

NEVCO, INC.  MODEL 9605 EXTERIOR ELECTRONIC

MULTI-SPORT SCOREBOARD ACCESSORY

2.4	ACCESSORIES

A.	Provide each scoreboard or accessory with control cable of length required.  Electrical junction boxes, conduits, mounting hardware, and other accessories as required for installation are to be provided by others.

*****  Various optional accessories can be provided with football scoreboards to enhance the installation.  Most accessories are connected wired or wirelessly (Receiver sold separately) with the scoreboard control unit.  Select required accessories from the following. *****

*****  Use the following to specify Model 9605 , a multi-sport bi-directional timing board for timed sporting events.  *****

B.	Type:  Exterior, electronic, timer with LED display for bi-directional time; Model 9605  as manufactured by Nevco, Inc.

1.	Size:  [6 feet long x 3 feet x 8 inches deep.] [1.8 m long x .91 mm high x 203 mm]

2.	Approximate weight:  [60 pounds] [27 kg].

3.	White on black captions, [8 inches] [203 mm] high:  "TIME".

4.	LED timing display:  High intensity red, amber or translucent white [18 inches] [457 mm] high digits.  Timing is bi-directional.

a.	Up count with minutes and seconds separated by colon.

b.	Down count with minutes and seconds separated by colon.  During final minute, 1/10th seconds are displayed separated by decimal.

c.	Capable of displaying time of day after disconnection from control center.

5.	Power requirement: 120/240 Volts, 0.4/0.2 amps 50/60 Hz.