(HIDDEN TEXT AVAILABLE)

SECTION 11 66 43

NEVCO MODEL 4700 SERIES

INTERIOR ELECTRONIC HOCKEY ACCESSORIES

******************************************************************************

*****  Including the following paragraph to specify hockey shots on goal electronic unit Model 4765 to be connected to scoreboard control center. Choose either [NL],[RL] [ETN] option  *****

A.	Shots on goal unit:  Electronic unit with LED display for shots on goals for each team;  Model 4765 as manufactured by Nevco Scoreboard Company.

1.	Size:  [60 inches long x 36 inches high x 8 inches deep] [1524 mm long x 914 mm high x 203 mm deep].

2.	Approximate hanging weight:  [45 pounds] [20 kg].

3.	Captions  [6 inches] [152 mm] high "Home" and "Guests".

4.	Non-illuminated captions:  [6 inches] [152 mm] high "shots on goal".

5.	LED shots on goal displays:  Super Bright Amber [13 inches] [330 mm] high digits.

6.	Power requirement:  All options included: 60 Watts, MAX, 90 to 240 Volts AC w/Power Factor Correction.

******************************************************************************

*****  Include the following to specify goal lights to operate as part of total hockey scoreboard system and connected to scoreboard control center.  *****

B.	Hockey goal light system:  Provide system of two goal light displays connected to electronic modules and two operator switches; Model GL-H5/GJS-5 as manufactured by Nevco Scoreboard Company.

1.	Display:  Red and green low voltage lights mounted behind goals and illuminated in accordance with hockey rules.

2.	Electronic module:  [18 x 19-3/4 x 4 inches] [457 x 502 x 102 mm] aluminum box pre-wired with solid state electronics and [12 feet] [3.7 m] power cord.

3.	Operator switches:  Two hand-held judge's switches.

4.	Electrical power:  48 watts, 120 volts 60Hz, requires earth ground.