SECTION 11 66 43

NEVCO, INC. MODEL 4 FACE 4750

INTERIOR ELECTRONIC HOCKEY SCOREBOARD AND ACCESSORIES

PART 1 - GENERAL

1.1	SUMMARY

A.	Section includes:  Interior, electronic, hockey and 4 face center hung hockey scoreboard[s] including control center, and other accessories for complete functional installation.

*****  List other specification sections dealing with work directly related to this section such as the following.  *****

1.	Section 11 66 23	Gymnasium Equipment

2.	Section 26 20 00	Low Voltage Electrical Distribution

3.	Section 27 41 16	Integrated Audio-Video Systems

4.	Section 10 14 63	Electronic Message Signage

1.2	REFERENCES

****  List by number and full title reference standards referred to in remainder of the specification section.  *****

A.	American Society for Testing and Materials (ASTM) Publications:

1.	ASTM B221 - Aluminum-Alloy Extruded Bar, Rod, Wire, Shape, and Tube.

- National Electrical Code.

- Federal Communications Commission, Part 15 Rules & Regulations.

- UL and C-UL Standard for Electric Signs

1.3 SUBMITTALS

- Provide in accordance with Section 01 33 00 - Submittal Procedures:

- To minimize the environmental impact of multiple paper copies, product installation prints, instructions and diagrams of manufacturer will be submitted in a paperless fashion.  The end user shall receive all pertinent hard-copy documentation at delivery.

- Product data for scoreboards, controls, and accessories shall include descriptions of control functions etc.

- Installation drawings, face layout, dimensions, construction, electrical wiring diagrams, and method of anchorage.  (Paperless when applicable).

- Copy of guarantee required by Paragraph 1.5 for review by Architect.  (Paperless when applicable).

- Manufacturer's installation instructions. (Paperless when applicable).

- Finish Samples.

1.4	QUALITY ASSURANCE

A.	Source limitation:  All components including scoreboard, control center, control cable, and other accessories and installation hardware shall be products of a single manufacturer.

B.	Manufacturer qualifications:  Company specializing in manufacturing electronic scoreboards with 10 years minimum successful world-wide experience.

C.	Scoreboards and other electrical components shall be certified for use in United States and Canada by Underwriter Laboratories, (UL), Inc. and shall bear either UL or C-UL label only.

D.	Scoreboards and other electrical components shall be electrically grounded in accordance with National Electrical Code (NEC), Article 600.

1.5	GUARANTEE

A.	Provide under provisions of Section 01 78 00 - Closeout Submittals:  Guarantee to cover defects in materials and workmanship.

1.	Scoreboards, scoring tables, marquees, message centers, video boards* and Stadium Pro loudspeaker enclosures are guaranteed for a period of five (5) years from the date of invoice against defects in workmanship or materials.

**Video Board exclusions include 8815, 8825, 8835, 8845.

2.	Wireless components, portable scoreboards and solar power kit carry a two (2) year guarantee from date of invoice. Hand-held controls and switches carry a one (1) year guarantee from date of invoice. The Stadium Pro loudspeaker front printed scrim is guaranteed for one (1) year from the date of invoice. Video Board Models 8815, 8825, 8835, and 8845 are guaranteed for one (1) year from date of invoice, unless additional years of warranty is purchased. For products supplied by third-party suppliers (i.e. cameras, computers, computer monitors, radar guns, loudspeakers, amplifiers and associated electronics), Purchaser agrees to accept the manufacturer’s warranty, if any, in lieu of any warranty by Nevco.

3.	Lifetime telephone support.

PART 2 - PRODUCTS

2.1	ACCEPTABLE MANUFACTURERS

A.	Nevco, Inc, 301 East Harris Avenue, Greenville, Illinois 62246; 800-851-4040; www.nevco.com.

B.	Requests to use equivalent products of other manufacturers shall be submitted in accordance with Section 01 25 00 - Product Substitution Procedures.

2.2	MATERIALS

A.	Aluminum face and perimeter frame:  Fabricated from [0.050] [inch] [1.3] [mm] minimum thickness, ASTM B221 aluminum sheet.

B.	Finish:  Acrylic polyurethane paint.  Color as selected by Architect from manufacturer's standard range. [Color to be [No. 70 - Desert Tan] [No. 72 - Electronic Blue] [No. 73 - Maroon] [No. 74 - Forest Green] [No. 76 - Print Black] [No. 95 - Silver Gray] [No. 99 - Golden Yellow] [No. 102 - Team Orange] [No. 103 - Cardinal Red] [No. 104 - Medium Purple] [No. 120 - Teal Blue] [No. 121 - Midnight Blue] [No. 140 - Royal Blue] [No. 141 - Navy Blue] [No. 142 - Kelly Green]  as provided by Nevco, Inc.] [PMS Color No._____].

C.	Electronics:  Low voltage, solid state, 2-wire cable, multiplex system, quartz crystal controlled.

D.	Provide fiber optic communication interface to reduce threat of damage from electrical storms.

E.	LED (light emitting diode) units:  Seven-bar, segmented digits in protective aluminum cover, rated typical life 100,000 hours, and designed to provide excellent visibility from all angles and sides.

F.	Provide location specific universal power cord for world-wide installation.

G.	Control cable where required shall be UL listed, 2-wire, type RG-58/U, coaxial cable, [1/4 inch] [6 mm] diameter.

H.	Junction boxes where required:  Sheet metal box and cover, [4-1/2 x 2-1/8 x 2-1/8 inches] [114 x 54 x 54 mm] min. complying with NEMA standards.

I.	Powder coated tubular steel framework shall be included as standard equipment.  Additional signage and/or message center accessories shall be bolt-on options listed in other sections.

2.3	SCOREBOARDS

*****  Include the following to specify Model 4-FACE-4711-NL, a four-sided, suspended, hockey scoreboard with four identical panels each displaying time, goals scored, period, uniform numbers for players serving penalties and the penalty times.  Scoreboard can accommodate two penalty player uniform numbers and times per team.  *****

A.	Type:  Interior, suspended, four-sided, electronic, hockey scoreboard consisting of four identical panels with two integral horns each and LED displays for time, goals scored, period, uniform numbers for players serving penalties, and penalty times; Model 4-FACE-4750-NL (base) as manufactured by Nevco, Inc.  Rear-lit (RL) caption plates or Electronic Team Names (ETN) are optional and scoreboard shall be capable of in-the-field retrofit.  Only LED lighting shall be used for rear-lit captions, incandescent lighting excluded.  No captions shall be applied directly to the face of the scoreboard.  All caption plates will be changeable and made of polyvinylchloride with vinyl lettering applied.

1.	Shape:  Square box with tapered faces, [145 inches] [3683 mm] square top sloping to [114 inches] [2896 mm] square bottom x [72 inches] [1829 mm] high.

2.	Construction:  Aluminum panels with steel suspension frame..

*****  As an option, 4-FACE-4711-NL Scoreboard can be provided with solid bottom.  *****

3.	Bottom:  Provide flat bottom panel finished to match scoreboard; Model B-7 Bottom as manufactured by Nevco, Inc.

4.	Approximate hanging weight:  [1070 pounds] [486 kg].

5.	Back lighted captions:

a.	[6 inches] [152 mm] high "Home", "Guests", "shots on goal", and two "penalty" captions.

6.	Non-illuminated captions:  [6 inches] [152 mm] high "period".

7.	LED displays:

a.	Timing:  Super Bright Red [13 inches] [330 mm] high digits.

b.	Team scores:  Super Bright Amber [13 inches] [330 mm] high digits.

c.	Period:  Super Bright Amber [9 inches] [229 mm] high digit.

d.	Shots on goal for each team:  Super Bright Amber [9 inches] [229 mm] high digits for each team.

e.	Two penalty times per team:  Super Bright Red [9 inches] [229 mm] high digits.

8.	Advertising or team/facility/mascot area:  1 ea. [36 x 12 inches] [914 x 305 mm] and 1 ea. [12x
12 inch] [ 305 x 305 mm]  [for Owner applied graphics or imprint].

9.	Power requirement: All options included: 184 Watts per face, MAX, 90 to 240 Volts AC w/Power Factor Correction..

2.4	ACCESSORIES

A.	Provide each scoreboard or accessory with control cable of length required.  Electrical junction boxes, conduits, mounting hardware, and other accessories as required for installation are to be provided by others.

***** Include the following to specify Electronic Team Names or Rear-lit captions with your Nevco scoreboard. *****

B.	Electronic Team Names: “HOME” and “GUEST” caption plates to be replaced with programmable Electronic Team Names as manufactured by Nevco, Inc.

1.	Specify changeable team names. (ETN) Shall not require controller upgrade, use of additional accessories or computer.

2.	Specify (R)ed or (A)mber ETN LED’s (Example: 27xx ETN-R)

C.	Provide rear-lit caption plate option. Specify (RL). (Model Example: 27xx-RL)

D.	Provide for optional Team Name in place of “HOME” if NL/RL is selected.

E.	Additional accessories include but are not limited to; please specify quantity required.

*****  Various optional accessories can be provided with basketball scoreboards to enhance the installation.  Most accessories are interfaced with the scoreboard control unit.  Select required accessories from the following.  *****

- Protective Nets/Screens.

- Nevco, Inc “A”, “AD”, or “ADL” signs including Artwork with unlimited amount of color.

- Nevco, Inc Locker Room Clocks.

- Nevco, Inc Full Color, Red or Amber Message Centers.

- Nevco, Inc Video Displays.

******************************************************************************

*****  Including the following paragraph to specify hockey shots on goal electronic unit Model 4765 to be connected to scoreboard control center. Choose either [NL],[RL] option  or  [NL]-[ETN] option  *****

F.	Shots on goal unit:  Electronic unit with LED display for shots on goals for each team;  Model 4765 as manufactured by Nevco, Inc.

1.	Size:  [60 inches long x 36 inches high x 8 inches deep] [1524 mm long x 914 mm high x 203 mm deep].

2.	Approximate hanging weight:  [45 pounds] [20 kg].

3.	Captions  [6 inches] [152 mm] high "Home" and "Guests".

4.	Non-illuminated captions:  [6 inches] [152 mm] high "shots on goal".

5.	LED shots on goal displays:  Super Bright Amber [13 inches] [330 mm] high digits.

6.	Power requirement:  All options included: 60 Watts, MAX, 90 to 240 Volts AC w/Power Factor Correction.

******************************************************************************

*****  Include the following to specify goal lights to operate as part of total hockey scoreboard system and connected to scoreboard control center.  *****

G.	Hockey goal light system:  Provide system of two goal light displays connected to electronic modules and two operator switches; Model GL-H5/GJS-5 as manufactured by Nevco, Inc.

1.	Display:  Red and green low voltage lights mounted behind goals and illuminated in accordance with hockey rules.

2.	Electronic module:  [18 x 19-3/4 x 4 inches] [457 x 502 x 102 mm] aluminum box pre-wired with solid state electronics and [12 feet] [3.7 m] power cord.

3.	Operator switches:  Two hand-held judge's switches.

4.	Electrical power:  48 watts, 120 volts 60Hz, requires earth ground.

- Four Face Advertising / Message Center support structure frame. Upper and Lower versions.
1.	Welded tubular steel construction.
2.	Powder coated black finish.
3.	Shall bolt-on to existing 4700 series four face structure.
4.	Available in standard heights of 12, 24, or 36 Inches [305, 610, or 915  mm] and widths 	dependant on upper or lower structure.

2.5 CONTROL CENTER

*****  Nevco manufacturers the following control centers for operating scoreboards and other accessories.  Refer to Nevco product literature for appropriate control centers for specific scoreboards and electronic accessories.

MPC - Universal wired control center with extensive control features and capacity to operate both scoreboard and accessories.

MPCW - Universal wireless version of MPC Control Center with receiver unit mounted at scoreboard.

MPCX - Wireless, battery operated control center with receiver unit mounted at scoreboard.

*****  Include the following to specify MPC Control Center.  *****

A.	Type:  Wired, microprocessor based operator's control center designed to operate different models of scoreboard by interchange of keyboard overlay; Model MPC as manufactured by Nevco, Inc.  Console will operate earlier scoreboards from Nevco, Inc.

1.	Console:  High impact, break-resistant gray plastic [11 x 9-1/2 x 4-1/8 inches] [279 x 241 x 105 mm].

2.	Features:

a.	Provide with LED displays, lithium cell battery backup to maintain scoreboard memory and time of day, self test mode, power on-off switch, alternate time control, and multiple scoreboard operation.

b.	Split and raised 40 key keyboard, internal beeper acknowledging each entry, and bookmark capabilities.

c.	Keyboard overlays for scoreboard or accessory.

d.	Remote hand-held main time switch with integral horn button.

e.	[25 feet] [7.6 m] control cable with connectors.

f.	Timer features:  Time of day display, multiple time out timers with warning, interval horn, up-count auto stop with horn, and 1/10th second display during last minute.

g.	Dimmer control for scoreboard.

3.	Power requirements:  120 volts, 12 watts, 50/60 Hz.

4.	Provide option of battery supply for control operation if utility power not available.

5.	Provide carrying case for control center, cable, and hand-held switch; Model CC-3 as manufactured by Nevco, Inc.

a.	Size:  [18-1/2 x 14-1/2 x 6 inches] [470 x 368 x 152 mm].

b.	Construction:  Double wall, high density black polyethylene with padded interior, mechanical latches, and hinges.

B.	Type:  Wireless, microprocessor based, operator's control center with receiver unit mounted at scoreboard and designed to operate different models of scoreboard by interchange of keyboard overlay; Model MPCW as manufactured by Nevco, Inc.  Console will operate earlier scoreboards from Nevco, Inc.

1.	Unit shall comply with Part 15 of FCC Rules regarding interference.

2.	Console:  High impact, break-resistant gray plastic [11 x 9-1/2 x 4-1/8 inches] [279 x 241 x 105 mm].

3.	Features:

a.	Control can be used to operate both wireless and wired scoreboards.

b.	Power on-off switch.

c.	Split and raised 40 key keyboards, internal beeper acknowledging each entry, and bookmark capabilities.

d.	Keyboard overlays for scoreboard or accessory.

e.	Remote hand-held main time switch with integral horn button.

f.	Provide with LED displays, lithium cell battery backup to maintain scoreboard memory and time of day, self test mode, power on-off switch, alternate time control, and multiple scoreboard operation.

g.	Timer features:  Time of day display, multiple time out timers with warning, interval horn, upcount auto stop with horn, and 1/10th second display during last minute.

h.	Dimmer control for scoreboard.

4.	Receiver:  Sturdy impact resistant construction, [6 x 4 x 1.5 inches] [1.52 x 102 x 38 mm] with [4 inch] [102 mm] antenna and mounted at scoreboard.

5.	Maximum range:  [1,000 feet] [305 m] from control center to receiver.

6.	Receiver shall require no additional source of power or separate control cable

6.	Power adapters:  Provide for each control center and receiver.

a.	Input:  120 volts, 0.4 amps, 50/60 Hz.

b.	Output:  9 volts, 1.67 amps, 15 watts.

7.	Provide option of battery supply for control operation if utility power not available.

8.	Provide carrying case for control center and hand-held switch; Model CC-3 as manufactured by Nevco, Inc.

a.	Size:  [18-1/2 x 14-1/2 x 6 inches] [470 x 368 x 152 mm].

b.	Construction:  Double wall, high density black polyethylene with padded interior, mechanical latches, and hinges.

******************************************************************************

*****  Include the following to specify MPCX Control Center.  *****

C.	Type:  Handheld wireless, basic, AA battery operated, sport specific, control center with receiver unit mounted at scoreboard; Model MPCX2 as manufactured by Nevco, Inc.  Control will have operability with earlier scoreboards from Nevco, Inc.

1.	Unit shall comply with Part 15 of FCC Rules and Regulations.

2.	Control unit:  High impact, break-resistant black ABS plastic Size: 3-1/4” x 5-1/2” x 7/8” (.08 x .14 x .02 m)

3.	Features:

a.	Wireless operation within [1000 feet] [305 m].

b.	Operate multiple scoreboards simultaneously.

c.	System allows multiple controllers to link to individual scoreboards.

d.	High visibility LCD display with a sealed keyboard.

e.	Long battery life with indicator; include two AA batteries.

f.	Single hand operation with a no slip grip.

g.	Built-in belt clip.

h.	Wireless signal strength meter and internal antenna.

4.	Receiver:  Injection molded case, [5-1/2 by 3-3/4 by 2 inches] [140 by 95 by 51 mm] mounted at scoreboard.

5.	Maximum range:  [1,000 feet] [305 m] from control center to receiver.

6.	Receiver shall require no additional source of power or separate control cable

6.	Power adapters:  Provide for each scoreboard receiver.

a.	Input:  120 volts, 0.4 amps, 50/60 Hz.

b.	Output:  9 volts, 1.67 amps, 15 watts.

7.	Provide carrying case for up to two control centers, Model CC-4 as manufactured by Nevco, Inc.

a.	Size:  [18-1/2 x 14-1/2 x 6 inches] [470 x 368 x 152 mm].

b.	Construction:  Double wall, high density black polyethylene with padded interior, mechanical latches, and hinges.

PART 3 - EXECUTION

3.1	PREPARATION

A.	Verify exact scoreboard and control center quantities and junction box locations with Architect.

B.	Coordinate require ments for electrical power, wall blocking, auxiliary framing and supports, suspension cables, and other components to be provided under other Specification Sections to ensure adequate provisions are made for complete, functional installation of scoreboards.  [Ensure that building roof structure has been designed for loads of suspended scoreboards.]

C.	Coordinate scoreboard electrical requirements to ensure proper power source, conduit, wiring, and boxes are provided.  Prior to installation, verify type and location of power supply.

3.2	INSTALLATION

A.	Install scoreboards and accessories in accordance with manufacturer's instructions and approved installation drawings.

B.	Before installation, field test scoreboards and accessories for operating functions.  Ensure that scoreboards accurately perform all operations.  Correct deficiencies.

C.	Rigidly mount scoreboards and accessories level and plumb with brackets and fasteners.

D.	Clean exposed surfaces.

E.	Protect scoreboards and finishes from other construction operations.

3.3	DEMONSTRATING AND TRAINING

A.	In accordance with Section 01 75 00 - Starting, Adjusting, and Demonstrating, provide demonstration and training session for Owner's representative covering operation and maintenance of electronic scoreboard.

END OF SECTION