# SECTION 10 14 64

# ELECTRONIC MONOCHROME MESSAGE CENTERS

*****  Since 1934 Nevco has been manufacturing superior quality scoreboards.  Today Nevco provides a broad range of indoor and outdoor, electronic scoreboards for all types of sporting events.  In addition to scoreboards Nevco provides electronic LED video displays and message centers for indoor and outdoor applications.

This guide can be used to prepare a specification for incorporating Nevco 16 MM Monochrome Message Center, an electronic, red or amber LED message center with 16 mm resolution for both indoor and outdoor applications into a competitively bid construction project.

The specification section is organized by placing information in three standard parts:

PART 1 - GENERAL			Describes administrative and procedural requirements.

PART 2 - PRODUCTS		Describes materials, message centers, controls, and accessories to be incorporated into the construction project.

PART 3 - EXECUTION		Describes how the message centers will be installed at the construction site.

Throughout this product guide specification, references are made to other specification sections that might be contained in the project manual.  These references are presented as examples and coordination reminders.  For each project, these references will need to be revised to reflect actual sections being used.

Within the specification text, Imperial dimensions are presented first in brackets followed by System International Metric (SI) equivalents also in brackets.  Depending on project requirements, either the Imperial or the SI metric equivalents will need to be deleted.

The specifier will need to edit this product specification for a specific project to reflect the options and applications being used.  The guide section has been written so that most editing can be accomplished by deleting unnecessary products, requirements, and options.  Options are indicated by  [   ].  Notes to assist the specifier in selecting options and editing the specification guide are printed in bold and indicated with  *****.  For final editing, all brackets and notes will need to be deleted from the guide.

PART 1 - GENERAL

1.1		SUMMARY

A.	Section includes:  Electronic, monochrome, LED message center with 10 mm pitch including control software for operating message center and other accessories for complete functional installation.

*****  List other specification sections dealing with work directly related to this section such as the following.  *****

1.	Section 01 10 00 - Summary:  Provision [by Owner] [others under separate contract to Owner] of computer and basic software to control message center.

*****  Message centers can be installed indoors or outdoors.  Structural components to support message centers, attachment hardware, electrical supply, conduit, wiring, and other auxiliary components are not provided by Nevco and need to be designed by Architect, detailed on Drawings, and specified in other sections.  *****

2.	Section 03 30 00 - Cast-in-Place Concrete:  Concrete footings for posts supporting exterior message centers.

3.	Section [__][__][__]:  Structural [walls to receive wall mounted message center.] [roof framing to receive suspended message center display.]  [Steel posts and other structural framing to support message centers.]

4.	Section 26 05 26  - Grounding and Bonding:  Grounding of exterior message centers.

5.	Section 26 [___][___]:  Electrical supply, conduit, wiring, and other electrical components for message centers and controls.

*****  Message centers can be installed in conjunction with an electronic scoreboard.  Contact Nevco if message center is to be used in combination with electronic scoreboard.  *****

6.	Section 11 66 43 Interior Scoreboards: 11 68 43 Exterior Scoreboards:  Scoreboards installed in conjunction with message centers.

1.2		REFERENCES

****  List by number and full title reference standards referred to in remainder of the specification section.  *****

A.	American Society for Testing and Materials (ASTM) Publications:

1.	ASTM B221 - Aluminum-Alloy Extruded Bar, Rod, Wire, Shape, and Tube.

- National Electrical Code.

- Federal Communications Commission, Part 15 Rules & Regulations.

- UL and C-UL Standard for Electric Signs

1.3		DEFINITIONS

A.	Light emitting diode (LED):  Semi-conductor diode that converts DC electric energy into electromagnetic radiation at a visible frequency.  Color of the LED is a function of emitted wavelength.

*****  Luminosity or brightness is measured in NITS.  For example, the luminosity of a typical computer display is 200 to 300 NITS.  *****

B.	Luminosity:  Brightness of light emitting image.  Unit of measure is NIT equal to one candela per square meter.

C.	Pitch:  Spacing or distance between two elements such as pixels.

****  The term "pixel" is a combination of "picture" and "element".  Pixels can be colored print dots or points of light used to form printed or video images.  *****

D.	Pixel:  The smallest element of a display which can be assigned a color.  Message center pixels are LED blocks.

E.	Resolution:  Indication of amount of detail or sharpness of an image.  Typically measured by the number of pixels displayed horizontally and vertically.

1.4 SUBMITTALS

- Provide in accordance with Section 01 33 00 - Submittal Procedures:

- To minimize the environmental impact of multiple paper copies, product installation prints, instructions and diagrams of manufacturer will be submitted in a paperless fashion.  The end user shall receive all pertinent hard-copy documentation at delivery.

- Product data for scoreboards, controls, and accessories shall include descriptions of control functions etc.

- Installation drawings, face layout, dimensions, construction, electrical wiring diagrams, and method of anchorage.  (Paperless when applicable).

- Copy of guarantee required by Paragraph 1.5 for review by Architect.  (Paperless when applicable).

- Manufacturer's installation instructions. (Paperless when applicable).

- Finish Samples.

1.4		QUALITY ASSURANCE

A.	Message center shall be designed for interior or exterior installation with weatherproof housing.

B.	Message center and other electrical components shall be certified for use in United States and Canada by Underwriters Laboratories (UL) and shall bear UL label.

C.	Message center and other electrical components shall be electrically grounded in accordance with National Electrical Code (NEC), Article 600.

*****  Include the following paragraph if message center is have wireless communications option. *****

1.	Wireless control unit shall comply with Part 15 of FCC Rules.

1.5		GUARANTEE

*****  Nevco message centers are provided with 5 years parts and labor guarantee.  *****

A.	Provide under provisions of Section 01 78 00 - Closeout Submittals:  5 years parts and labor guarantee for message center to cover defects in materials and workmanship.

PART 2 - PRODUCTS

2.1		ACCEPTABLE MANUFACTURERS

A.	Nevco, 301 East Harris Avenue, Greenville, Illinois 62246; 800-851-4040; www.nevco.com.

B.	Requests to use equivalent products of other manufacturers shall be submitted in accordance with Section 01 25 00 - Product Substitution Procedures.

2.2		MATERIALS

A.	Aluminum housing:  Fabricated from [0.050 inch] [1.27 mm] minimum thickness, ASTM B221 aluminum sheet.  Finish with acrylic polyurethane paint with ultraviolet inhibitor providing long lasting finish.

B.	LED (light emitting diode): Designed to provide excellent visibility from all angles and sides.

D.	Control cable:  Fiber optic or Ethernet, or Wireless Ethernet

C.	Fasteners, anchors, brackets, and other exposed hardware not supplied shall be corrosion resistant.

2.3		MONOCHROME MESSAGE CENTER

*****  Message centers can be installed indoors and outdoors.  Both single-sided and double-sided message centers are available.  *****

A.	Type:  [Exterior] [Interior], electronic, monochrome, LED, [single-sided] [double-sided] message center to be [wall mounted] [roof suspended] [free standing, post supported] [installed in combination with scoreboard] [_____]; 10 MM Full Color LED Message Center as manufactured by Nevco.

*****  10 MM Monochrome LED Message Center is provided in three heights and several widths.  Available heights and the number of message lines with 2.75 inches (70 mm) high characters is as follows:

2 feet (0.6 m) high with six message lines.

3 feet (.9 m) high with nine message lines.

4 feet (1.2 m) high with twelve message lines.

Refer to Nevco product literature for available widths and corresponding weights.  Double-sided message centers weigh twice as much and typically mount back to back on supporting structure.  They are configured as parent / child.  Edit the following paragraphs to reflect size of message center required.  Viewing Area is the number of pixels horizontal multiplied by the pixel pitch multiplied by the  number of  pixels vertical multiplied by the pixel pitch *****

1.	Viewing area:  [_____] pixels high x [_____] pixels wide.

2.	Approximate hanging weight:  _____ pounds [_____ kg].

3.	Message center depth:  [8 inches] [203 mm].

4.	Number of message lines with [2.75 inches] [70 mm] high characters:  [6] [9] [12].

*****  16 MM Monochrome LED Message Center is fabricated with numerous LED display elements or pixels spaced at approximately 0.63 inch (16 mm).  Please specify either red or amber LED pixels.  *****

5.	LED display elements:  [Full Color] SMD LED.

6.	LED pixel pitch:  [0.39 inch] [10 mm].

7.	Pixel Brightness:  6,000 NITS (cd/m2).

8.	Color capacity:  68 Billion.

9.	Viewing angles:  170 degrees horizontal and vertical.

10.	Pixel design:  Each pixel shall have protective louver.

B.	Power requirements:

1.	Input:  85-265 VAC.

*****  Depending on message center size, power consumption varies from 150 watts to 828 watts. Refer to Nevco product literature for applicable power consumption values.  *****

2.	Power consumption:  [_____] watts.

C.	Ambient operating temperature: -40 to 150 degrees F

D.	Should replacement of a block of pixels be necessary, message center shall be pixel by pixel adjustable to compensate for the effects of age degradation.

E.	Maintenance access:  Front

2.4		MESSAGE CENTER CONTROL SYSTEM

A.	Provide operating software and other accessories to use with computer and basic software [specified in other sections] [provided by [Owner] [others under separate contract with Owner].

1.	Message center shall be controlled from remote location by one person.

- Access to message center control shall be limited by a hardware security key.

- Access shall be further limited by customer protected password.

2.	Operating System:  Windows based, 64-bit capable.

*****  Message center can be connected to control computer by either CAT5 Ethernet wire, Fiber Optic cable link or Wireless Ethernet communications.  *****

*****  Message center can be connected to control computer by either CAT5 Ethernet wire, Fiber Optic cable link or Wireless Ethernet communications.  *****

B.	Communications link:  [Fiber Optic cable] [CAT5 Ethernet cable] [Wireless Ethernet system.]

1.	Status of communications between Composer Software and Message Center shall be constantly monitored.

C.	Graphic capabilities:  Text, animation, logos, multiple fonts, moving messages, and video file capability.

1.	Each Message Center “project file” shall contain all the required information to successfully establish message frames on a given message center, from user created “playlists’.  These frames and playlists shall have user definable attributes to comply with local sign laws regarding timing and presentation.

D.	Input:  Control software shall have ability to import AVI, BMP, JPG and GIF image files from Adobe, Corel, and other standard computer graphics software.

E.	Control software shall consist of a single MMI window.  Switching between windows and programs to affect message center properties shall not be allowed.

F.	Proof of Performance:  Software will provide an event record as proof of performance.

G.	Display dimming:  16 levels controlled manually.

- Automatic scheduling:  Provide for creating schedule to display stored messages.

2.5		ACCESSORIES

A.	Provide message center with control cable of required length in installation drawings.  Outdoor includes temperature sensor / photocell.  Electrical junction boxes, conduits, mounting hardware, and other accessories as required for installation are to be provided by others.

PART 3 - EXECUTION

3.1		PREPARATION

A.	Coordinate provision of message center with:

1.	Design and construction of [wall blocking] [auxiliary framing and supports] [suspension cables] [concrete footings and steel posts and other structural framing] [exterior wall] [monument sign] [_____] detailed on Drawings and specified in other sections.

2.	Design and provision of electrical supply, conduit, wiring, disconnect switch, weatherproof receiver and circuit boxes, and other electrical components for powering message center and controls.

B.	Prior to installation, verify type and location of power supply.

3.2		INSTALLATION

A.	Before installation, field test message center for operating functions.  Ensure that message center accurately performs all operations.  Correct deficiencies.

B.	Install message center and accessories in accordance with manufacturer's instructions and approved installation drawings.

C.	Rigidly mount message center level and plumb with fasteners.

D.	Protect message center from other construction operations.

3.3		DEMONSTRATING AND TRAINING

A.	In accordance with Section 01 75 50 - Starting, Adjusting, and Demonstrating, provide demonstration and training session for Owner's representative covering operation and maintenance of electronic message center.

1.  Provide operating manual with clear easy to follow instructions. Manufacturer will offer instruction and demonstration at the factory.  Provide technical consultation by phone to answer any questions.

.

# END OF SECTION